## Slide 1
ARCHITECTURE BRIEFING
Cloud & 5G telemetry
and command relay
Extending WildNav ground control beyond WiFi range
Prepared for leadership review — August 2026

## Slide 2
Today: ground control only works over WiFi
WiFi-only control
The operator must stay on the same WiFi network as the drone to see telemetry or send any command.
Blind once out of range
Beyond WiFi, the ground team loses live telemetry and has no way to intervene mid-flight.
WiFi range
Ground team — no link
WildNav — Cloud & 5G Relay
2

## Slide 3
Add a 5G cloud path
Monitor and control the drone from anywhere — not just on WiFi
Drone (Jetson)
5G network
Cloud (MQTT)
Dashboard
Commands (STOP / LOITER / RTL) travel the same path in reverse.
WildNav — Cloud & 5G Relay
3

## Slide 4
What this unlocks
Live telemetry, anywhere
Position, battery, and mission status visible from any internet connection, not just local WiFi.
Remote command & control
Issue STOP, LOITER, or RTL commands mid-flight — not monitoring-only.
Safety-first by design
The aircraft's own failsafes stay independent and active underneath this link at all times.
Near-zero added cost
Cloud messaging fits inside a free-tier budget at the current fleet size.
WildNav — Cloud & 5G Relay
4

## Slide 5
By the numbers
$0/mo
cloud messaging cost
at 1-3 drones
<300ms
typical command
round-trip over 5G
1-3
drones supported at the
current design tier
24/7
continuous live
monitoring capability
WildNav — Cloud & 5G Relay
5

## Slide 6
Why it matters for WildNav
Unlocks BVLOS-style operation
Missions can run beyond WiFi range — critical for remote or wilderness deployments.
Scales without new hardware cost
The same cloud path supports a growing fleet; only the broker tier changes.
Built to extend
Historical playback, larger fleets, and richer telemetry can layer on top of this foundation later.
WildNav — Cloud & 5G Relay
6

## Slide 7
Technical architecture
How the system is built

## Slide 8
Data flow: device to cloud to dashboard, and back
Jetson (drone)
publishes over 5G
5G / cellular
outbound-only, NAT'd
MQTT broker
HiveMQ Cloud / AWS IoT
Ground dashboard
browser via MQTT-WS
→ telemetry, status, heartbeat
■ Navy — telemetry & heartbeat (drone → cloud → dashboard)
■ Cyan — commands: STOP / LOITER / RTL (dashboard → cloud → drone), confirmed by an ack
The 5G modem is outbound-only (carrier NAT) — nothing can dial into the drone, so every message is a push through the broker, in both directions.
WildNav — Cloud & 5G Relay
8

## Slide 9
How the link is built: MQTT over TLS
TLS 8883, authenticated
Every connection is encrypted; each drone has its own certificate-based identity.
One topic set per drone, per purpose
wildnav/<id>/telemetry, /status, /cmd, /cmd_ack — each drone can only touch its own topics.
At-least-once delivery
QoS1 with persistent sessions — a dropped connection replays queued messages instead of losing them.
WildNav — Cloud & 5G Relay
9

## Slide 10
Commands are confirmed, not just sent
Operator sends
STOP / LOITER / RTL
Drone receives
& executes
Drone sends an ack
back to the dashboard
No acknowledgment within ~3 seconds → the dashboard flags the command as unconfirmed.
STOP, LOITER, and RTL are always honored even if delayed — the worst case is a redundant safe action, never a harmful one.
WildNav — Cloud & 5G Relay
10

## Slide 11
Designed for a link that will drop out
Local backlog buffer
The Jetson buffers telemetry locally and replays it after a reconnect, capped by age.
Automatic reconnect
Exponential backoff avoids hammering the network or draining battery on a bad connection.
Flight continues regardless
If the cloud link drops, the mission already loaded on the drone continues; the aircraft's own failsafes remain active underneath.
WildNav — Cloud & 5G Relay
11

## Slide 12
Defense in depth
Per-drone certificates
No shared credentials — each aircraft authenticates independently.
Scoped permissions
Broker rules restrict each drone to its own topics — one compromised device can't see or command another.
Command signing
Planned hardening: an application-level signature on commands, independent of broker auth.
WildNav — Cloud & 5G Relay
12

## Slide 13
Broker choice is a config value, not a redesign
Broker | Billing model | Est. cost at 1-3 drones
HiveMQ Cloud (free tier) | Connections + traffic | $0 / month
EMQX Cloud Serverless | Session-minutes + traffic | $0 / month
AWS IoT Core | Per-message + connectivity | ~$8–$16 / month
Default: HiveMQ Cloud free tier. AWS IoT Core is supported when native AWS integration (IAM, Timestream, fleet-management tools) outweighs the added per-message cost — the relay code only needs an endpoint and credentials to switch.
WildNav — Cloud & 5G Relay
13

## Slide 14
Next steps
1. Build cloud_relay.py on the Jetson
2. Provision the broker and per-drone credentials
3. Integrate MQTT-over-WebSocket into the dashboard
4. Field test over real 5G coverage
Questions & discussion